HOUSEHOLD WATER MONITORING SYSTEM

        KARTHI G

        KRISHNA PRIYA S

        SOWMYA K

ABSTRACT

Water is one of the most important substances on earth.People nowadays always want something that can make their life easier. This project is used to define the water monitoring systems such as water quantity monitoring and water quality monitoring.By using Wireless Sensor Technology we avoid the huge amount of water is being wasted by uncontrolled use of houses.The microcontroller based water quantity monitoring is used to indicate the amount of water is used by the consumers.Sensor based water quality monitoring will check the water quality by using these parameters such as the turbidity,bacteria detection and conductivity.Our motivation is to prevent the water by using technologies and the monitoring system uses daily life device like laptop or mobile phones.

CONTENTS

SL NO:	CHAPTER	PAGE NO:
1	INTRODUCTION	1
2	EXISTING SYSTEM	2
3	PROPOSED SYSTEM	3
4	SYSTEM ARCHITECTURE	5
5	MODULE DESCRIPTION	7
6	CONCLUSION	8
7	REFERENCES	9

INTRODUCTION

Water is a limited resource and is essential for agriculture, industry and for creatures existence on earth including human beings .Lots of people don’t realize the true importance of drinking enough water every day. More water are wasted by many uncontrolled way. This problem is quietly related to poor water allocation, inefficient use, and lack of adequate and integrated water management. Therefore, efficient use and water monitoring are potential constraint for home or office water management system.
Managing water consumption is not an easy task, but it is vital for life preservation. Most of us do not know how much water we actually use, and conserving is difficult when you don’t have an understanding of your current water usage. Here we are proposing a smart water meter that connects to a water pipe to track use .Even if you pay a flat rate for your water, this might help you to keep your energy bills down, tracking and storing the water usage so users can keep an eye out for water they are using daily. This is a fully fledged Internet of Things device, so it'll report back to the cloud via your Wi-Fi. Stored on a remote server, data about your water usage is ready to be viewed using mobile phones.
The smart water meter can be attached to any residential water pipe, where it captures data on how much water a household uses. A Wi-Fi module built in to the device sends all of its data to cloud, breaking water habits down into digestible graphs of total water consumption and progress towards water-saving goals.

        1

EXISTING SYSTEM

Water metering is the process of measuring the water use. Water meter is a device which measures the volume of water flowing through a pipe line system. Generally water meters are provided to measure the volume of water used by residential and commercial buildings that are supplied with water by a public water supply system. Water meters are also used at a water source to determine flow through a particular portion of the system. Normally, water meters measure flow in cubic meters (m3).
Mechanical meters are positive displacement flow meters. They operate by isolating and counting known volumes of a fluid, while feeding it through the meter. By counting the number of passed isolated volumes, flow measurement is obtained. These meters are suited for measurement of clear water with little turbidity and generally less expensive than non-mechanical types. Hence these are commonly used in urban water supply systems. However, they have a higher maintenance requirement.

Working Principle:
An impellor is rotated by water passing through the meter. The rotation of impeller is then translated into a volumetric reading. The mechanism is calibrated by an adjustable device that is preset and security sealed. These meters are available in various sizes and require full water flow in the pipeline during measurement.

Disadvantages of Existing system:
- Mechanical parts can be damaged, making frequent accuracy testing necessary.
- Prone to wear in silty water, resulting in loss of accuracy and frequent need for replacement.
- Some head loss possible.
- Single purpose.
- Lack of efficient monitoring system able to check both quantity and quality as well.

2

PROPOSED SYSTEM
Access to clean water is something that most us probably take for granted . The proposed smart water meter that connects to both your pipes and your Wi-Fi network. Meanwhile, a slew of sensors baked into the box itself constantly keep tabs on the rate of water flow and all the foreign particulate bits floating around in that water.
The proposed smart water meter has two main goals – Alert user to know how much water you are using, helping you to create better water habits in your daily routines and the check the quality of water.
The sensors that check both quantity and basic quality of water is inserted in the main pipe of our house and flow sensor is attached to each and every taps inside the house, where it captures data on how much water is consumed by the respective taps. It keeps track of how much water is passing through the tap and sends the information to a cloud - based server through a microcontroller. The information collected can be accessed by water authority as well as users through a web browser .This helps the authority to track the water consumption details of each houses more easily and can compute the water bills electronically.
Another advantage of this system is the leakage detection. If the summation of water quantity sensed in each tap and the total quantity reading shown in sensor attached to the main pipe has a huge variation, then we can say that a leakage is occurred.

3

Advantages of proposed system
- Encourages sustainability in our way of life.
- Creates saving habits in future generations.
- Helps household economy.
- Helps landlords manage water bills.
- Helps monitor remote water pipes.
- Adoption of our innovative technology in water conservation program.
- Easy to install; plugs into any ½ “ pipe or, using the right fitting, to any ⅜” or ¾” pipe.
- Recommended for showers, water taps, and backyard, or main water supply.
- Connects to Internet via Wi-Fi.
- The data is transmitted via WiFi to the Cloud, so the user can review it on a web or mobile device in real-time.
- The data generated can be shared in a social way where you can share your achievements with your friends, neighbors.

4

4.SYSTEM ARCHITECTURE

MICROCONTROLLER

Flow

CLOUD

DOMESTIC
LINE
MAIN
UNIT
CONSUMER
SENSORS
Internet
Coagulation
Bacteria
Detection
Conductivity

SYSTEM

5

Water Quality Sensors
Coagulation sensor
        This measures both dissolved and suspended solids. There are six major types of
        suspended solids; silt, clay, soil runoff, plankton, industrial waste, and sewage.
Bacteria detection sensor
It generally checks for indicator bacteria (for example, total coliform, fecal coliform or Escherichia coli) and can indicate the presence or absence of disease-causing bacteria.
Conductivity
Ions increase the water's ability to conduct electricity. Common ions in water that conduct electrical current include sodium, chloride, calcium, and magnesium. Because dissolved salts and other inorganic chemicals conduct electrical current, conductivity increases as salinity increases.
Water Flow sensor
The arduino flow sensor works on the principle of “Hall Effect”. It is utilized in the flow sensor using a small fan/propeller shaped rotor which is placed in the path of the liquid flowing .The liquid thus pushes against the fins of the rotor, causing it to rotate. The shaft of the rotor is connected to a hall effect sensor. It is an arrangement of a current flowing coil and a magnet connected to the shaft of the rotor. Thus a voltage/pulse is induced as this rotor rotates. This is due to the changing magnetic field caused by the magnet attached to the rotor shaft. We measure the number of pulses using an arduino.
WiFi Module - ESP8266
This is a self contained SOC with integrated TCP/IP protocol stack that can give any microcontroller access to your WiFi network
Microcontroller: Arduino mega
The Arduino Mega is a microcontroller board based on the ATmega1280.Data collected by sensors are processed and then send to the cloud via a communication medium.
Cloud based server: php and mysql
It is a user interface in the form of website that maintains the water quantity and quality details and is owned by water authority ,also users can view the data.
Operating System : Ubuntu

6

MODULE DESCRIPTION

1. User Module:
In this module consumers can check their water usage details.
2. Administrator Module:
This is the main module in the proposed project. The administrator can read and write information about any users. The administrator can also update, create and delete the records and also can generate online water bills.
The following are the sub module in the administrator module.
- Register consumer : Allow the administrator to register new consumers.
- Consumption details : Allow administrator to maintain the water consumption details.
- Bill issue : Here administrator issues the bills to the consumers based on their consumption.

7

CONCLUSION

Water is one of the most important basic needs for all living beings. But unfortunately a huge amount of water is being wasted by uncontrolled use. The main issue that is being addressed in this project is about developing an efficient wireless sensor network (WSN) based water monitoring system. In this way of monitoring water ,the data about quantity used and basic quality of water is collected.
Finally the proposed water monitoring system of smart homes concept will be completed by using wireless sensor technology. By using the monitoring system we can easily prevent the water and the water will be save to our generation.

8

REFERENCE

[1] International Research Journal of Engineering and Technology (IRJET)
        Volume: 02 Issue: 04 | July-2015
[2] Planning of water quality monitoring systems, Technical Report Series No.3
[3] Guidelines on water meters ,Report no.RDSO/WKS/2015/5 March– 2015
[4] Home automation for dummies (Google Books)

9